## Slide 1: Ventjet Dispersion Analysis for Jack Rabbit III Modeling Exercise
March 2022
Amy Shen, Derek Miller, Seshu Dharmavaram
EHS Central Process Safety
Air Products

## Slide 2: Overview of models
Ventjet is a new engineering model for atmospheric dispersion of various gases, including light gases, neutral gases, and heavy gases. It has been broadly validated against multiple measurements from wind tunnel and field experiments as well as CFD simulations.
According to the model inputs (pressure/temperature etc.), Spicer-Miller model (also called “APFlow”) is used to calculate the effective source conditions for high pressure ammonia releases. It is developed for prediction of two-phase flashing flow across openings and works well across a wide range of materials and conditions.
Early mixing of the two-phase aerosol with air is calculated to determine the conditions at location where all the ammonia liquid becomes vapor by conservation of mass, momentum and enthalpy. The conditions can then be used in Ventjet for dispersion analysis.

## Slide 3: Effective source conditions
Model input conditions from JRIII document Table 1 are input to APFlow to calculate the effective source conditions which are then used for further analysis
Trial | Release rate (kg/s) | Temp. (K) | Molar vapor fraction | Velocity (m/s) | Diameter (m) | Droplet diameter (μm)
FLADIS 9 | 0.4 | 239.67 | 0.163 | 56.3 | 0.041 | 151.8
FLADIS 16 | 0.226 | 239.67 | 0.171 | 47.4 | 0.034 | 141.6
FLADIS 24 | 0.46 | 239.67 | 0.139 | 38.8 | 0.049 | 171.3
DT1 | 80.0 | 237.54 | 0.214 | 72.5 | 0.615 | 118.3
DT2 | 117.0 | 237.56 | 0.226 | 75.3 | 0.749 | 112.4
DT4 | 108.0 | 237.41 | 0.238 | 86.4 | 0.692 | 109.3
Note: rainouts for Desert Tortoise trials are neglected in the calculations.

## Slide 4: Conditions at location where all the ammonia liquid has vaporized
Early mixing calculations are done to bridge the two-phase aerosol outputs from APFlow and the inputs to Ventjet gas dispersion analysis.
Trial | Downstream distance (m) | Molar NH3 conc. (%) | Temp. (K) | Velocity (m/s) | Diameter (m) | Total mixture mass flowrate (kg/s)
FLADIS 9 | 2.6 | 11.76 | 204.1 | 7.83 | 0.737 | 5.49
FLADIS 16 | 2.1 | 11.95 | 204.3 | 6.98 | 0.582 | 3.05
FLADIS 24 | 3.2 | 11.69 | 204.0 | 6.24 | 0.887 | 6.35
DT1 | 29.2 | 13.92 | 205.0 | 11.94 | 8.201 | 918.01
DT2 | 36.3 | 14.26 | 205.3 | 11.04 | 10.194 | 1308.42
DT4 | 33.7 | 14.67 | 205.6 | 11.58 | 9.473 | 1172.29

## Slide 5: FLADIS test data vs. Ventjet predictions
Ventjet predictions match quite well with the FLADIS trial 9/16/24 test data at all the three sensor locations.

## Slide 6: Desert Tortoise test data vs. Ventjet predictions
For DT1/DT2/DT4, Ventjet predictions tend to overpredict the near field concentration at 100 m and to under-predict a little bit the far-field concentration at 800 m.

## Slide 7: Reference
D. Miller, E. Vyazmina, A. Shen, E. Lutostansky. Gone with the wind: Ventjet is a new engineering model for atmospheric dispersion. Process safety progress, 2021.
T. Spicer, D. Miller. Quantifying the mass discharge rate of flashing two phase releases through simple holes to the atmosphere. Process Safety Progress, vol.37, No.3, 2018.

## Slide 8: Thank you tell me more